## Slide 1: Fail-Slow at Scale Evidence of Hardware Performance Faults in Large Production Systems
1
2
3
4
5
6
12
10
11
7
8
9
Haryadi S. Gunawi1, Riza O. Suminto1, Russell Sears2, Casey Golliher2, Swaminathan Sundararaman3, Xing Lin4, Tim Emami4, Weiguang Sheng5, Nematollah Bidokhti5, Caitie McCaffrey6, Gary Grider7, Parks M. Fields7, Kevin Harms8, Robert B. Ross8, Andree Jacobson9, Robert Ricci10, Kirk Webb10, Peter Alvaro11, H. Birali Runesha12, Mingzhe Hao1, Huaicheng Li1

## Slide 2: 1st anecdote
“…a 1Gb NIC card on a machine that suddenly only transmits at 1 kbps,
this slow machine caused a chain reaction upstream
in such a way that the 100 node cluster began to crawl at a snail's pace.”
Cascading
impact!
Slow hardware!
fail-stop
fail-partial
fail-transient

## Slide 3: More anecdotes? All hardware?
Disk throughput dropped to 100 KB/s due to vibration
SSDs stalled for seconds due to firmware bugs
Memory cards degraded to 25% speed due to a loose NVDIMM connection
CPUs ran in 50% speed due to lack of power

## Slide 4: Fail-slow Hardware
Hardware that is still running and functional but in a degraded mode, significantly slower than its expected performance
In existing literature:
  “fail-stutter” [Arpaci-Dusseau(s), HotOS ’11]
  “gray failure” [Huang et al. @ HotOS ’17]
  “limp mode” [Do et al. @ SoCC ’13, Gunawi et al. @ SoCC ’14, Kasick et al. @ FAST ’10]
  (But only 8 stories per paper on avg. and mixed with SW issues)

## Slide 5: Believe it?
Fail-slow hardware is “not” real.
It is rare.
Yes, it’s real!
Let’s write a paper together

## Slide 6: Evidences from …
Fail-slow
at
scale

## Slide 7: Data and Methodology
101 reports
  Unformatted text
  Written by engineers and operators (who still remember the incidents)
  2000-2017 (mostly after 2010)
  Limitations and challenges:
    No hardware-level performance logs [in formatted text]
    No large-scale statistical analysis
Methodology
  An institution reports a unique set of root causes
    “A corrupt buffer that slows down the networking card (causing packet loss and retransmission)”
    Counted as 1 report from the institution (although might have happened many times)

## Slide 9
Varying root causes
  Internal causes: firmware bugs, device errors
  External causes: temperature, power, environment, and configuration
Faults convert
  Fail-stop, -partial, -transient  fail-slow
Varying symptoms
  Permanent, transient, and partial slowdown, and transient stop
Cascading nature
  Cascading root causes
  Cascading impacts
Rare but deadly
  Long time to detect (hours to months)
Summary of findings

## Slide 10
Varying root causes
Internal
root
causes
External
root
causes

## Slide 11
Varying root causes
  Internal
    Device errors/wearouts
      Ex: SSD read disturb/retry + page reconstruction  longer latency and more load
read(page X, Vth=v1)
read(page X, Vth=v2)
read(page X, Vth=v3)
read(page X, Vth=v4)
4x slower!
RAIN: Redundant Array of Independent NAND
read p1
ECC
error
Picture from http://slideplayer.com/slide/10095910/
Voltage shift
read p0
read p2
read P012
read p0
read p2
read P012
read p0
read p2
read P012
read retries!

## Slide 12
Varying root causes
  Internal
    Device errors
    Firmware bugs
      [No details, proprietary component]
      SSD firmware bugs throttled μs to ms read performance
      Another example: 840 EVO firmware bugs [2014]
https://www.anandtech.com/show/8550/samsung-acknowledges-the-ssd-840-evo-read-performance-bug-fix-is-on-the-way
Throughput collapse

## Slide 13
Varying root causes
  Internal Device errors and firmware bugs [More details in paper]
SSD | Disk | Memory | Network | Processors
Firmware bugs (us to ms read performance, internal metadata writes triggering assertion); Read retries with different voltages; RAIN/parity-based read reconstruction; Heavy GC in partially-failing SSD (not all chips are created equal); Broken parallelism by suboptimal wear-leveling; Hot temperature to wear-outs, repeated erases, and reduced space; Write amplification. | Firmware bugs (jitters, occasional timeouts, read retries, read-after-write mode); Device wearouts (disabling bad platters); Weak heads (gunk/dust accumulates between disk heads and platters); and other external factors such as temperature and vibration. | Address errors causing expensive ECC checks and repairs; Reduced space causing more cache hits; Loose NVDIMM connection; SRAM control-path errors causing recurrent reboots (transient stop). | Firmware bugs (buggy routing algorithm, multicast bad performance); NIC driver bugs; buggy switch-NIC auto-negotiation; Starving from electrons (bad design specification); bad VSCEL laser; Bitflips in device buffer; Loss packets cause TCP retries and collapse. | Buggy BIOS firmware down-clocking CPUs; Other external causes such as hot temperature and lack of power.

## Slide 14
Varying root causes
  Internal [Device errors, firmware bugs]
  External
    Temperature
Cold-air-under-the-floor system
Hot temperature
 Corrupt packets
 Heavy TCP retransmission
Faster SSD
wearouts,
bad Vth 
more read retries
Slower disk performance
at bottom of the rack
(read-after-write mode)

## Slide 15
Varying root causes
  Internal [Device errors, firmware bugs]
  External
    Temperature
    Power
4 machines, 2 power supplies
100%
100%
100%
100%
1 dead power  50% CPU speed
50%
50%
50%
50%
Power-hungry applications 
throttling neighboring CPUs
throttled
Power-hungry
throttled
throttled

## Slide 16
Varying root causes
  Internal [Device errors, firmware bugs]
  External
    Temperature
    Power
    Environment
      Altitude, pinched cables, etc.
    Configuration
      A BIOS incorrectly downclocking CPUs of new machines
      Initialization code disabled processor cache

## Slide 17
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert
  Fail-transient  fail-slow
Bit flips 
ECC repair
(error masking)
read
Okay if rare
But, frequent errors
frequent error-masking/repair
repair latency becomes the common case

## Slide 18
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert
  Fail-transient  fail-slow
  Fail-partial  fail-slow
Picture from https://flashdba.com/2014/06/20/understanding-flash-blocks-pages-and-program-erases/
“Not all chips are created equal”
(some chips die faster)
Aggregate
exposed space (e.g. 1 TB)
Overprovisioned space
Reduced
overprovisioned space
Reduced overprovisioned space
More frequent GCs  Slow SSD
Fail-partial
SSD Internals

## Slide 19
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert
  Fail-transient  fail-slow
  Fail-partial  fail-slow
Custom memory chips that mask (hide) bad addresses
X GB
Fail-
partial
Exposed space
<
X GB
<<
X GB
Higher
cache misses
(fail-slow)

## Slide 20
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms
  Permanent slowdown
Time

## Slide 21
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms
  Permanent slowdown
  Transient slowdown
Vibration
Disk performance
CPU performance

## Slide 22
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms
  Permanent slowdown
  Transient slowdown
  Partial slowdown
Fast
reads
Slow
reads
(ECC repairs)
Small packets (fast)
>1500-byte packets (very slow)
[Buggy firmware/config related to jumbo frames]

## Slide 23
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms
  Permanent slowdown
  Transient slowdown
  Partial slowdown
  Transient stop
Time
A bad batch of SSDs “disappeared” and then reappeared
A firmware bug triggered hardware assertion failure
Host Bus Adapter recurrent resets
Uncorrectable bit flips in SRAM control paths

## Slide 24
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms Permanent, transient, partial slowdown and transient stop
Cascading nature
  Cascading root causes
Disk throughput collapses to KB/s
Fans
normal
speed
One died
Other fans
maximum speed
Noise and
vibration
Bad disks? No!

## Slide 25
M1
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms Permanent, transient, partial slowdown and transient stop
Cascading nature
  Cascading root causes
  Cascading impacts e.g. in Hadoop MapReduce
A fast map task
(read locally)
R1
R2
R3
Slow!!
All reducers are slow
(“no” stragglers  no Speculative Execution)
Use (lock-up) task slots in
healthy machines for a long time
Eventually no free task slots
 Cluster collapse
Slow
NIC
Shuffle

## Slide 26
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms Permanent, transient, partial slowdown and transient stop
Cascading nature
  Cascading root causes
  Cascading impacts
1 job/hour !!!
~170 jobs/hour
Facebook Hadoop Jobs, 30 nodes
with 1 slow NIC
[From PBSE @ SoCC ’17]

## Slide 27
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms Permanent, transient, partial slowdown and transient stop
Cascading nature
Rare but deadly
  13% detected in hours
  13% in days
  11% in weeks
  17% in months
  (50% unknown)
Why?
External causes and cascading nature (vibrationslow disk); offline testing passes
No full-stack monitoring/correlation hot temperature  slow CPUs  slow Hadoop  debug Hadoop logs?
Rare? Ignore?

## Slide 28
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms Permanent, transient, partial slowdown and transient stop
Cascading nature
Rare but deadly
Suggestions to vendors,
operators, and systems designers
+

## Slide 29
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert Fail-stop, -transient, -partial  fail-slow
Varying symptoms Permanent, transient, partial slowdown and transient stop
Cascading nature
Rare but deadly
+ Fail-slow hardware
Modern, advanced systems
Thank you! Questions?
Conclusion:

## Slide 30: EXTRA

## Slide 31: Suggestions
To vendors:
  Make the implicits explicit
    Frequent error masking  hard errors
  Record/expose device-level performance statistics
To operators:
  Online diagnosis
    (39% root causes are external)
  Full-stack monitoring
  Full-stack statistical correlation
To systems designers:
  Make the implicits explicit
    Jobs retried “infinite” time
  Convert fail-slow to fail-stop? (challenging)
  Fail-slow fault injections

## Slide 33: Operators
Cannot use application bandwidth check (all are affected)
Hadoop, not fully tail/limpware tolerant??
1 job/hour !!!
~170 jobs/hour
Facebook Hadoop Jobs, 30 nodes

## Slide 34
100%
100%
100%
100%
Varying root causes Device errors, firmware, temperature, power, environment, configuration
Faults convert
  Fail-stop  fail-slow
    Fail-stop power  fail-slow CPUs
    Fail-stop disk  fail-slow RAID
Fail-stop
50%
50%
50%
50%
Fail-slow