## Slide 1: Tiny-Tail Flash Near-Perfect Elimination of Garbage Collection Tail Latencies in NAND SSDs
Shiqin Yan, Huaicheng Li, Mingzhe Hao,
Michael Hao Tong, Swaminathan Sundararaman*,
Andrew Chien, and Haryadi S. Gunawi
ceres.cs.uchicago.edu
*

## Slide 2
“if your read is stuck behind an erase you may have wait 10s of milliseconds. That’s a 100x increase in latency variance”
The Tail at Scale [CACM’13]
http://www.zdnet.com/article/why-ssds-dont-perform/
https://storagemojo.com/2015/06/03/why-its-hard-to-meet-slas-with-ssds/

## Slide 3
Reads + Writes
Clean/Empty SSD
0.3ms
Time
Read Latency
Convert to CDF
Read Latency
Percentile
100%
80%
NoGC
0.3ms

## Slide 4
Reads + Writes
0.3ms
Aged/Full
SSD
80%
100%
Read Latency
3%
≥5 ms
NoGC
with GC
Percentile
0.3ms
Time
Read Latency
80ms
Long tail !
Objective: cut tail
80 ms!

## Slide 5: How GC delays read I/Os?
Read
A
B
A
B
delayed!
A GC moves tens of valid pages!
which makes channel/chips busy for tens of ms !
fast
Channel
Chip

## Slide 6: How to cut tail latencies?
RAID:
Full Stripe Read
Tail-tolerant techniques in distributed/storage systems:
Leverage redundancy to cut tail!
C = XOR
(A, B, P)
fast
tail!
A
C
B
Slow / busy
A
P
B
C

## Slide 7: How to cut tails in SSD?
SSD:
Error rate increases  RAIN (Redundant Array of Independent NAND)
Similarly, we leverage RAIN to cut “tails”!
Full Stripe Read
C = XOR
(B, C, P)
A
C
B
slow!
fast
A
B
C
P
GC

## Slide 8
Plane-Blocking GC
GC-Tolerant Read
Rotating GC
GC-Tolerant Flush
Contribution
RAIN
(Parity-based Redundancy)
Current SSD
technology:
New
techniques:

## Slide 9: Results
100%
95%
0.3ms
80ms
CDF (Percentile)
Latency
Base
NoGC
+Plane-Blocking
+GC-Tolerant Read
+Rotating GC

## Slide 10
100%
95%
0.3ms
80ms
CDF (Percentile)
Latency
Tiny tail!
Between 99 - 99.99th percentiles:
ttFlash 1-3x slower than NoGC
Base 5-138x slower than NoGC
Overall results achieved:

## Slide 11: Outline
  Introduction
  Background
  Tiny-Tail Flash Design
  Evaluation, limitations, conclusion

## Slide 12: SSD Internals
…
…
…
…
Chip
Die [0]
Plane[0]
…
Die [1]
Chip
Plane[N]
C0
C1
CN

## Slide 13: SSD Internals
C0
…
C1
…
CN
…
…
Plane
Valid Page
Block[0]
…
Block[N]
Chip
Plane
…

## Slide 14
for (1 … # of valid pages):
1. read to controller
(check with ECC)
2. write to another block
…
Empty block
Old block
SSD Controller
14
1
2
blocked!
GCed pages block the channel

## Slide 15
3. Erase the old block
…
Empty block
Old block
SSD Controller
15
Erase!
Erase operation block the plane

## Slide 16
…
16
A
B
C
blocked!
GCing plane
Channel blocking GC
“Base” approach

## Slide 17
100%
95%
0.3ms
80ms
Latency
NoGC
Base (Channel-Blocking)
CDF (Percentile)

## Slide 18: Outline
  Introduction
  Background
  Tiny-Tail Flash Design
    Plane-Blocking GC
    GC-Tolerant Read
    Rotating GC
    GC-Tolerant Flush
  Evaluation, limitations, conclusion

## Slide 19
…
19
…
A
A
B
C
B
C
blocked!
Base:
Channel
Blocking
Plane
Blocking
GCing plane
GCing plane
Leverage
intra-plane copyback support
Unblock
the channel

## Slide 20
…
Empty block
Old block
SSD Controller
20
Read
Page
A
B
C
Base GC Logic:
for (every valid page)
1. flash read+write
(over channel)
2. wait
Plane Blocking
GC Logic:
for (every valid page)
flash read+write
(inside plane)
serve other
user I/Os
1
2
Overlap
intra-plane copyback with
channel usage for other non-GCing planes
Plane Blocking
“Intra-plane
copyback”
1
2
1
2

## Slide 21
100%
95%
0.3ms
80ms
Latency
NoGC
+Plane-Blocking
3% of I/Os
are blocked
by GC
Only
1.5%
Base (Channel-Blocking)

## Slide 22
  Issue 1: No ECC check for garbage-collected pages
    (will discuss later)
  Issue 2:
Y
X
Read
delayed!
Read
Read
Z
X
Y
Z
GC-ing plane
still blocks

## Slide 23: Outline
  Introduction
  Background
  Tiny-Tail Flash Design
    Plane-Blocking GC
    RAIN + GC-Tolerant Read
    Rotating GC
    GC-Tolerant Flush
  Evaluation, limitations, conclusion

## Slide 24: RAIN
PG1
PG2
C3
LPN (Logical Page #)
Static mapping:
LPN0  C[0]PG[0]
LPN1  C[1]PG[0]
…
Add parity:
LPN 0, 1, 2  P0,1,2
Rotating parity as RAID 5
PG0
C0
C1
C2
0
1
2
P0,1,2
3
4
P3,4,5
5
P6,7,8
7
8
6

## Slide 25
Full Stripe Read
2 = XOR
(0, 1, P0,1,2)
0
2
1
tail
GC
0
1
2
P0,1,2
fast
0
2
1
Read in parallel
+ XOR cost
~0.01 ms
Wait for GC
2 to 10s of ms
vs.
RAIN enables GC-Tolerant Read

## Slide 26
0
1
2
P0,1,2
2
Partial stripe read:
slow!
2 = XOR
(0, 1, P0,1,2)
Must generate extra
N-1 reads!
Add contention to other N -1 channels and planes
Convert to full stripe if:
Textra-reads < TGC
GC-Tolerant Read
Issue: partial stripe read

## Slide 27
Base
100%
95%
0.3ms
80ms
CDF (Percentile)
Latency
NoGC
+Plane-Blocking
+GC-Tolerant Read
0.5%

## Slide 28
One parity  cut one tail
Can’t cut two tails!
0
1
2
P0,1,2
Full-stripe read
0
2
1
2 tails!
DOES NOT HELP!
GC
GC
GC
Issue: more than 1 GCs
in a plane group?
PG0

## Slide 29: Outline
  Introduction
  Background
  Tiny-Tail Flash Design
    Plane-Blocking GC
    GC-Tolerant Read
    Rotating GC
    GC-Tolerant Flush
  Evaluation, limitations, conclusion

## Slide 30
0
1
2
P0,1,2
Rotating GC:
Anytime, at most 1 plane per plane group can perform GC
Postpone!
PG0

## Slide 31
0
1
2
P0,1,2
Rotating GC:
Anytime, at most 1 plane per plane group can perform GC
Rotating!
PG0

## Slide 32
0
1
2
P0,1,2
Rotating GC:
Anytime, at most 1 plane per plane group can perform GC
Concurrent GCs in different PGs are permitted.
PG0
PG1
PG2

## Slide 33
+Rotating GC
Why still tiny tails?
Small/partial-stripe read
 Sometimes may be better to wait for GC than adding extra reads/contentions!
100%
95%
0.3ms
80ms
CDF (Percentile)
Latency
0.5%
Tiny tail!

## Slide 34: Outline
  Tiny-Tail Flash Design
    Plane-Blocking GC
    GC-Tolerant Read
    Rotating GC
    GC-Tolerant Flush (in paper)
  Evaluation
  Limitations
  conclusion

## Slide 35: Implementation
SSDsim (~2500 LOC)
  Device simulator
VSSIM (~900 LOC)
  QEMU/KVM-based
  Run Linux and applications
OpenSSD
  Many limitations of the simple programming model
Future: ttFlash on OpenChannel SSD

## Slide 36: Evaluation
Simulator: SSDsim (verified against hardware)
Workload: 6 real-world traces from Microsoft Windows
Settings and SSD parameters:
  SSD size: 256GB, plane group width = 8 planes (1 parity, 7 data)

## Slide 37
100%
95%
0.3ms
80ms
Latency
NoGC
+Plane-Blocking
+GC-Tolerant Read
+Rotating GC
CDF (Percentile)
Developer Tools Release Server Trace
Base
99.99th
ttFlash
Result:
99.99th percentile:
ttFlash 3x slower than NoGC
Base 138x slower than NoGC

## Slide 38
Evaluated on 6 windows workload traces with various characteristics
Reduced blocked I/Os (total) from 2 – 7% to 0.003 – 0.05%
99 – 99.99%: 1.0 – 2.6x slower for ttFlash and 5.6 – 138.2x for Base

## Slide 39: Other Evaluations
Filebench on VSSIM+ttFlash
  ttFlash achieves better average latency than base case
Vs. Preemptive GC
  ttFlash is more stable than semi-preemptive GC
    (If no idle time, preemptive GC will create GC backlogs, creating latency spikes)
Latency (s)
6
0
Elapsed time (s)
4522
4386
ttflash
stable

## Slide 40: Tradeoffs/Limitations
ttFlash depends on RAIN
  1 parity for N parallel pages/channels
  We set N = 8, so we lose one channel out of 8 channels.
  Average latencies are 1.09 – 1.33x slower than NoGC, No-RAIN case
RAID  more writes (P/E cycles)
  ttFlash increases P/E cycles by 15 – 18% for most of workloads
  Incur > 53% P/E cycles for TPCC, MSN (random write)
ECC is not checked during GC
  Suggest background scrubbing (read is fast & not as urgent as GC)
  Important note: in ttFlash, foreground/user reads are still ECC checked

## Slide 41: Tails under Write Bursts
Latency CDF w/ Write Bursts
Latency (ms)
Under write burst and at high watermark, ttFlash must dynamitcally disable Rotating GC to ensure there is always enough number of free pages.
80 ms
0
90%
20%
CDF (Percentile)
Base 64MB/s
ttFlash 64MB/s
ttFlash 55MB/s

## Slide 42
GC-induced
long tail
Plane-Blocking GC
GC-Tolerant Read
Rotating GC
GC-Tolerant Flush
Conclusion
Powerful Controller
RAIN (parity-based redundancy)
Capacitor-backed RAM
technology:
New techniques:
ttFlash
CDF (Percentile)
Latency
Between 99 - 99.99th percentiles:
ttFlash 1-3x slower than NoGC
Base 5-138x slower than NoGC
Overall results achieved:

## Slide 43: Thank you! Questions?
http://ucare.cs.uchicago.edu
https://ceres.uchicago.edu