## Slide 1: PBSE: A Robust Path-Based Speculative Execution for Data-Parallel Frameworks
Riza O. Suminto, Cesar A. Stuardo, Alexandra Clark, Huan Ke, Tanakorn Leesatapornwongsa, Bo Fu, Daniar H. Kurniawan, Vincentius Martin, Uma Maheswara Rao G., Haryadi S. Gunawi
Notes: I will talk about how one slow network card in cluster, can still drag your job performance, and our strategy to mitigate it through PBSE.

## Slide 2: Speculative Execution (SE) 101
fast
straggling
slow NIC
fast backup task
input data
map task
Notes: Tail tolerance is a must requirement in todays data-parallel framework.
A popular solution to mitigate tail latency, is to employ Speculative Execution (SE).
…..
Speculative Execution algorithm, works by detecting such straggler, and launch same backup task for this straggler.

## Slide 3: Is Hadoop always tail tolerant?
Normal (no slow NIC)
vs.
with 1 slow 1Mbps NIC
Facebook Hadoop jobs on 30 nodes
1 job/hour!!!
Many jobs cannot “escape” limping NIC
Why SE does not work??
172 job/hour
Notes: We found an important source of tail latencies that current SE cannot handle graciously, that is ``node-level degraded network''.
On a cluster of 30 machines, we run a workload of couple hundreds Hadoop jobs….
….
But when one of the node network card experience bandwidth degradation, thoughout the time, entire cluster throughput, collapsed to just one job per hour!

## Slide 4: Problem 1: No Straggler Detected
All slow  “No” straggler detected!
slow NIC
Notes: First, is no straggler detected.
Let see this MapReduce Shuffling example.
All mappers, shuffle to all reducers.
Unfortunately, M2 node has slow NIC.
Both reducers fetch from M1 quick, but really slow from M2.
However, SE algorithm will just assume that nothings wrong, since everyone is slow at the same pace!
Note that, M2 is fast, because it read input from local disk.
All reducers are slow, no straggler is detected, and no backup task is launched.

## Slide 5: Problem 2: Straggling Backup
Backup task is also straggling!
Many
more cases
slow NIC
fast
slow
blame!
Notes: Second problem, is when backup task is also straggling.
Suppose that the shuffling in the previous case is not all-to-all.
….
However, it will mistakenly blame the reducer as straggler, and decide to speculate the reducer.
The backup reducer will again hit the same degraded M2.
This could be avoided if M2 is the one that being speculated.

## Slide 6
Good
Resource contention
Heterogeneous resources
Not Robust
Node-level network degradation
  slow NIC and switches
Findings
Basic Hadoop SE (BaseSE)
Notes: These findings of many failed speculation pattern give us confirmation, that current Basic SE algorithm in Hadoop…

## Slide 7: What’s The Flaw?
Network limpware is not considered a fault model
Task != Path
  Slow paths are sometimes not exposed
  Path progresses are lumped into per-task scores
4 paths
2 scores
all
Slow!
Notes: Given the maturity of Hadoop, we believe that there are fundamental flaws that lead to existence of these SE loopholes.
The obvious flaw from our stories is that network degradation is not considered as fault model.
And when the this fault model is not incorporated, the concept of path is also not considered.
…
Therefore, all run slow, and SE never kick in.

## Slide 8: Path-Based SE (PBSE)
Intuition: A task is a collection of paths
[Now]
Progresses
of 4 paths:
M1R1
M1R2
  M2R1
  M2R2
[Before]
Progresses
of 2 tasks:
R1
R2
1
1. Path Diversity
2. Path Progress
3. Path Speculation
Notes: From that observation, we present our solution to the problem: path-based speculative execution (PBSE).
The intuition behind PBSE is that task is a collection of paths.
And with paths exposed, PBSE can do better speculation using following techniques:
Path diversity, diversifying task placement to enforce no potential SPOF.
Path progress, where instead of just task score, we also expose multiple data-path within a task. And,
Path-based speculation. Using path progress information, to better speculate next backup task.

## Slide 9: Contribution
Introduce node-level network degradation
  Real important fault model
Expose path progress
  Not just task progress
Develop path straggler detection & speculation
PBSE full integration to Hadoop
  Initial integration to QFS, Spark, & Flume
Notes: Our contribution can be summarized as follow:

## Slide 10: Outline
Intro
PBSE Techniques
  Path Diversity
  Path Progress
  Path-based Speculation
Implementation & Evaluation
Conclusion
Notes: There rest of my talk will be organized as follow:
Next, we will discuss more detail about PBSE Techniques.
…

## Slide 11: Path Diversity
Enforce no potential SPOF-node
  SPOF = single point of [tail-latency] failure
  (to compare progresses of diverse paths)
Notes: First technique in PBSE is Path Diversity.
Remember that Path is data transfers from one node to another.
Path Diversity, enforce that there should be NO potential Single Point of Tail-latency failure, or tail-SPOF.
It is necessary so that PBSE can compare progresses of diverse path.
Lets take a look at folowing example.
Here, M1 and M2 read input D1 and D2 that belong to the same remote datanode.
This datanode is a tail-SPOF, since if it slow, both M1 and M2 will all slow together.
With Path Diversity, PBSE force both map task to read from replica that belongs to different nodes, resulting in two distinct path.
Now, if D2 to M2 path is slow here, while D1 to M1 path is fast, PBSE can assume that the D2 node is the bottleneck.
Same technique also applies in reducer write phase.
If their first datanode to write is same and unfortunately slow, the rest of their write path will also slow.
PBSE enforce that, the first write-pipeline nodes that choosen by reducers are as diverse as possible.

## Slide 12: Path Progress
Each task reports path progresses/bandwidths
  (not just report task scores)
Path progress can reveal the culprit
[Now]
4 Paths:
R1O1
O1O1’
  R2O2
  O2O2’
[Now]
4 Paths:
M1R1
M1R2
  M2R1
  M2R2
[Before]
2 Tasks:
R1
R2
[Before]
2 Tasks:
R1
R2
No Straggler
Actual straggler!
Notes: Second technique is Path Progress.
Lets go back to previous Shuffling example.
As I mentioned in previous slides, in Basic SE, task progress is represented by one score per task.
…
Basic SE algorithm, will not detect any stragler, because task score R1 and R2 are increasing at the same slow pace.
Task score hides the fact that there are actually 4 data transfer path that going on, and two path from M2 node is straggling.
…
The concept of path progress also hold in other MapReduce stages, such as reducer write phase here.
Before, to detect straggler, we again rely on the very same task score, that also being used for shuffling phase.
But in PBSE, each data path along the write pipeline will also be reported as individual path progresses, rather than lumped into task score.
By exposing and comparing these detailed, point-to-point, path progresses, PBSE can accurately reveal the true culprit behind straggler.

## Slide 13: Path-based Speculation
Use knowledge of previous failing paths
  (don’t always blame the task/stage, blame the bottleneck)
Notes: We now discuss about Path-based speculation
Similar to basic Hadoop SE, PBSE detection algorithm is per-job and runs for every MapReduce stage.
Using knowledge of previous failing paths, PBSE can do informed recovery.
Such that, rather than always blaming the task or phase, it will blame the actual bottleneck instead.
In case where there are 2 posibilities of recovery, PBSE will try the cheapest recovery strategy first.
If its turn out wrong, PBSE will perform the second recovery.
We call this Dynamic Retries, in constrast with basic SE where retry is usually limited just once.
Keep in mind that PBSE runs side by side with the basic SE.
The latter handles task stragglers, while PBSE handles path stragglers.

## Slide 14: Outline
Intro
PBSE Techniques
Implementation & Evaluation
Conclusion

## Slide 15: Hadoop + PBSE
6000+ LOC over Hadoop/HDFS 2.7.1
  3200 LOC in Application Manager
  1400 LOC in Task Management
  1400 LOC in HDFS

## Slide 16: PBSE vs BaseSE
150 Jobs Facebook Trace
15 nodes
One 1-Mbps NIC
speedup
escape
tail-SPOF
no tail
Notes: We evaluate PBSE against the basic Hadoop SE, or what we call BaseSE.
…
And then we redo the experiment, but this time, we inject one NIC slowdown into the cluster.
Under this setup, BaseSE performance drops significantly.
Unluckiest job not finish until > 1h
…
PBSE, under the same setup, show a better performance.

## Slide 17: Varied Experiment
Varying:
  NIC degradations (60/30/10/1/0.1 Mbps)
  Workload (Facebook, Cloudera)
  Cluster size (15 to 60 nodes)
PBSE still gain speedups
speedup-bw
PBSE speedup at specific percentile of jobs
Notes: Next, under the same fault model, we try to vary some factor in our experiment, and check wether PBSE stil gain speedups over BaseSE.
…
In all this variations, we just inject one NIC degradation .
…
PBSE can still gain significant performance speedups over BaseSE.
This is again due to the fact that in BaseSE, many jobs is locked, and can not escape from the slow node.
PBSE, on the other hand, can quickly detect and failover from them.

## Slide 18: PBSE vs Other Strategies
Others:
  Vs. Other schedulers (Capacity / FIFO / Fair)
  Vs. Other SE solutions (Cloning / Aggressive / HRead)
PBSE wins in all scenarios
  We fix the fundamental flaws
  i.e. path-based, not task-based
PBSE Wins!
Notes: Next, we compare PBSE versus other strategies.
…
This confirms that the SE loopholes are not about scheduling problems.
Different schedulers does not eliminate tail latencies caused by the degraded NIC.
…
In summary, PBSE wins in all scenario, because we fix the fundamental flaws by leveraging path-based, not task-based.

## Slide 19: Beyond MapReduce
All data-parallel systems need robust tail tolerance
Notes: Beyond MapReduce, we believe…
…
So, to show generality of PBSE, we also analyzed Quantcast File System (QFS), Apache Spark, Flume, and S4.
We found that all of them suffer from the tail-SPOF problem.
Our initial integration of PBSE to Hadoop/QFS, Spark, and Flume stack showed that it speculates effectively, and cuts tail latencies.
% Spark (Figure \ref{fig-emore}b) has a built-in SE similar to Hadoop SE, hence it is prone to the same tail-SPOF issues (\sec\ref{sec-bug}).
% Flume (Figure \ref{fig-emore}c) uses a static timeout to detect slow channels (no path comparisons). If a channel's throughput falls below 1000 events/sec, a failover is triggered. If a NIC degrades to slightly above the threshold, the timeout is not triggered. resulting in a backlog of events.
% S4 (Figure \ref{fig-emore}d) has a similar static timeout to Flume. Worse, it has a shared queue design in the fan-out protocol. Thus, a slow recipient will cripple the sender in transferring data to the other recipients (a head-of-line blocking problem).

## Slide 20: Outline
Intro
PBSE Techniques
Implementation & Evaluation
Conclusion

## Slide 21: Conclusion
BaseSE
+
Resource Contention
BaseSE
+
Limping NIC
PBSE
+
Limping NIC
long tail latency!
can not escape tail
(Task abstraction)
(Path abstraction)
More Robust SE
Notes: BaseSE, can cut tail latencies well in the case of resource contention or heterogeneous resources.
However, under node-level network degradation, BaseSE that relies on task abstraction, is not robust enough.
Long tail letencies still happening, and many jobs can not escape the tail.
On the other hand, PBSE, by leveraging path abstraction, can effectively cut tail latencies caused by node-level network degradation, and provide more robust Speculative Execution.

## Slide 22: Thank you! Questions?
http://ucare.cs.uchicago.edu